## Slide 1: Inside the Social Network’s (Datacenter) Network
Arjun Roy, Hongyi Zeng, Jasmeet Bagga, George Porter, and Alex C. Snoeren
SIGCOMM 2015
Presented by Ye Tian for Course CS05112

## Slide 2: Overview
Facebook Datacenter
Provisioning
Traffic Engineering
Switching

## Slide 3: Datacenter Topology
Unit of deployment: cluster
  Conventional 3-tier topology
  Machines are connected to top-of-rack switch (RSW) with 10-Gpbs links
  Each RSW is connected by 10-Gbps links to 4 cluster switches (CSW)
  Servers connected by a same set of CSW is a cluster
CSWs are inter- connected with Fat Cats (FC)

## Slide 4: Servers
Web servers
MySQL servers
Cache
  Leader: handles cache coherency
  Follower: caches most read content
Hadoop servers: offline data mining
Multifeed servers: assemble news feed
All physical servers, no virtual servers

## Slide 5: Data Collection
Fbflows:
  Facebook’s monitoring system
  Two components: agents and taggers
  Agent
    1:30000 sampling rate
    On every machine
    Extract header information: src/dst IP addr., port, protocol
  Tagger
    On a subset of machins
    Annotate header with additional information such as rack and cluster

## Slide 6: Data Collection
Port mirroring
  Monitor hosts in five different racks
    Web server / Hadoop node / cache leader / cache follower / multifeed node
    tcpdump
  Collect data without loss

## Slide 7: Overview
Facebook Datacenter
Provisioning
Traffic Engineering
Switching

## Slide 8: Utilization
Access links (links between hosts and their RSW)
  Quite low: average 1-minute link utilization less than 1%
Links between RSW and CSW
  median utilization varies between 10–20% across clusters, with the busiest 5% of the links seeing 23–46% utilization.
Links between CSWs and FC
  Still high

## Slide 9: Locality and stability
Hadoop server traffic breakdown
  Show both rack- and cluster-level locality
  99.8% of all traffic sent by the server is destined to other Hadoop servers: 75.7% of that traffic is destined to servers in the same rack
  Hadoop server communicates with 1.5% of the other servers in the cluster—spread across 95% of the racks—though only 17% of the racks receive over 80% of the server’s traffic
consequence of a combination of job size and the distinct phases that a Hadoop job undergoes

## Slide 10: Locality and stability
web server traffic break down
  only a minimal amount of rack-local traffic is present
  inter-datacenter traffic is present in larger quantities (web)

## Slide 11: Locality and stability
Cache system traffic breakdown
  Frontend cache followers primarily send traffic in the form of responses to Web servers—intra-cluster traffic
  Cache leaders maintain coherency across clusters and the backing databases, engaging primarily in intra- and inter-datacenter traffic

## Slide 12: Traffic Matrix
Rack-to-rack, Hadoop cluster
  Strong diagonal
  cluster-wide uniformity outside the local rack accounts for intra-cluster traffic representing over 80% of Hadoop traffic
Map tasks are placed to maximize read locality, but there are a large number of concurrent jobs which means that it is possible that any given job will not fit entirely within a rack.

## Slide 13: Traffic Matrix
Frontend cluster
  Strong bipartite traffic pattern between the Web servers and the cache followers
  Web servers talk primarily to cache servers and vice versa, and servers of different types are deployed in distinct racks

## Slide 14: Implication
non-uniform fabric technologies that can deliver higher bandwidth to certain locations than others may find use.
stability of the traffic patterns suggest that rapid reconfigurability may not be as necessary as some have assumed.
lack of significant levels of intra-rack locality hints that RSWs (i.e., top-of-rack switches) that deliver something less than full non-blocking line-rate connectivity between all of their ports may be viable.

## Slide 15: Overview
Facebook Datacenter
Provisioning
Traffic Engineering
Switching

## Slide 16: Flow Characteristics
Flow size and duration

## Slide 17: Flow Characteristics
Hadoop server:
  Most flows are short and small
  70% of flows send less than 10 KB and last less than 10 seconds
Other servers:
  Connection pooling leads to long-lived connections with relatively low throughput.
  Connection pooling is prevalent in cache followers (leaders), and 40(25)% of flows exceeding our 10-minute capture period.

## Slide 18: Load Balancing
Method: examine the distribution of flow rates, aggregated by destination rack, per second over a two-minute period and compare each second to the next. Intuitively, the better the load balancing, the closer one second appears to the next.
Hadoop: poorly balanced
  widely varying rates
  Hadoop is likely to see a myriad jobs of varying sizes.

## Slide 19: Load Balancing
Frontend: well balanced
  distribution of per-second flow rates from a single cache follower node to distinct Web server racks during a two minute period are similar.
  distributions for each of the 120 seconds are similar, and all are relatively tight,

## Slide 20: Heavy Hitters
Heavy hitters: the minimum set of flows (or hosts, or racks in the aggregated case) that is responsible for 50% of the observed traffic volume (in bytes) over a fixed time period.
Number and size of heavy hitters in 1-ms intervals for each of flow(f), host(h), and rack(r) levels of aggregation

## Slide 21: Heavy Hitters
Persistence
  fraction of the heavy hitters that remain in subsequent time intervals.
  Heavy hitter persistence is low for individual flows (red)
  Host-level aggregation (green) fares little better
  Considering rack-level flows (blue), heavy hitters are particularly stable.

## Slide 22: Heavy Hitters
CDF of the fraction of a second’s overall heavy hitters that are instantaneously heavy in each 1/10/100-ms interval within the second
  Rack-level predictions are much more effective
  Host-level predictions are more useful for Web servers than cache nodes, but only the 100-ms case is more than 30% effective.

## Slide 23: Implication
Many existing techniques work by identifying heavy hitters and then treating them differently
  provisioning a circuit, moving them to a lightly loaded path, employing alternate buffering strategies
Benefits are limited
  Challenging to predict heavy hitters
  heavy hitters are frequently not particularly heavy for the vast majority of the period.

## Slide 24: Overview
Facebook Datacenter
Provisioning
Traffic Engineering
Switching

## Slide 25: Per-packet Feature
Median: 250 bytes
Hadoop server: almost all packets are either MTU length (1500 bytes) or TCP ACKs
Packet size distribution

## Slide 26: Arrival Pattern
Hadoop nodes and Web servers see an order-of- magnitude increase in flow intensity.
cache leaders see a slightly higher arrival rate than followers.
TCP SYN inter-arrival time

## Slide 27: Buffer Utilization
Buffer occupancies are non-trivial, and can be quite high in the Web-server case.

## Slide 28: Concurrent Flows
Web servers and cache hosts have 100s to 1000s of concurrent connections, while Hadoop nodes have approximately 25 concurrent connections on average

## Slide 29: Concurrent Flows
consider flows at the rack level
  the number of different racks with which an individual host is communicating with

## Slide 30: Review
Facebook’s datacenter fabric
Traffic locality
Heavy hitters