## Slide 1: B4: Experience with a Globally-Deployed Software Defined WAN
Sushant Jain, Alok Kumar, Subhasree Mandal, Joon Ong, et al.
ACM SIGCOMM, 2013
Presented by Ye Tian for Course CS05112

## Slide 2: Outline
Background
Design
Traffic Engineering
TE Protocol and OpenFlow
Evaluation

## Slide 3: Motivation
WAN links are typically provisioned to 30~40% average utilization.
  Deliver admirable reliability
  With over-provisioning and high-end routing gear
Google’s data center WAN
  We control the applications, servers, and the LANs all the way to the edge of the network
  Most bandwidth-intensive applications can adapt their transmission rate based on available capacity
  No more than a few dozen data center deployments, making central control of bandwidth feasible.

## Slide 4: Two WANs of Google
User-facing network
  peers with and exchanges traffic with other Internet domains at Google’s Edge Points of Presence (PoPs)
http://peering.google.com

## Slide 5: Two WANs of Google
The B4 WAN
  Provides connectivity among data centers
  First and largest SDN/OpenFlow deployments.
Making Google one of the largest ISPs in the world

## Slide 6: B4 Applications
Applications (increasing volume, decreasing latency sensitivity)
  user data copies to remote data center
  remote storage access for computation over inherently distributed data sources
  large-scale data push synchronizing state across multiple data centers.

## Slide 7: B4 Characteristics
Elastic bandwidth demands
  can tolerate periodic failures with temporary bandwidth reductions.
Moderate number of sites
  A few dozen
End application control
  Can control application priorities and control bursts, rather than overprovision
Cost sensitivity
  traditional WAN (30~40% overprovision) is prohibitively expensive.

## Slide 8: Outline
Background
Design
Traffic Engineering
TE Protocol and OpenFlow
Evaluation

## Slide 9: Overview
Each B4 site
  Switch hardware layer
  Site controller layer
    Consist of Network Control Servers (NCS), hosting both OpenFlow controllers (OFC) and Network Control Applications (NCAs).

## Slide 10: Overview
Global layer
  Centralized application: SDN Gateway and a central TE server
Each server cluster is a logical AS with a set of IP prefixes. Each cluster contains a set of BGP routers that peer with B4 switches at each WAN site.
Design choices
  Has to support existing distributed routing protocols
  Build one integrated, centralized service combining routing (e.g., ISIS functionality) and traffic engineering
  Deploy routing and traffic engineering as independent services, with the standard routing service deployed initially and central TE subsequently deployed as an overlay

## Slide 11: Overview
Each B4 site consists of multiple switches with potentially hundreds of individual ports linking to remote sites.
The TE abstracts each site into a single node with a single edge of given capacity to each remote site.
All traffic crossing a site-to-site edge must be evenly distributed across all its constituent links.
B4 routers employ a custom variant of ECMP hashing to achieve the necessary load balancing.

## Slide 12: Switch Design
Build B4 switch from multiple merchant silicon switch chips
  128-port 10GE switch with 24 16×10GE chips.
Contains an embedded Linux processor
  Run OpenFlow agent (OFA): translates OF messages into driver commands to set chip forwarding table entries.

## Slide 13: Network Control Functionality
Most B4 functionality runs on NCS in the site controller layer co-located with the switch hardware
  NCS and switches share a dedicated out-of-band control-plane network.
Paxos handles leader election for all control functionality.
Use a modified version of Onix as OpenFlow Control (OFC).
  Maintain Network Information Base (NIB)
OFAs maintain active connections to multiple OFCs, communication is active to only one OFC at a time and only a single OFC maintains state for a given set of switches.

## Slide 14: Routing
Open source Quagga for BGP/ISIS on NCS
Routing Application Proxy (RAP) as an SDN application to provide connectivity between Quagga and OF switches
  BGP/ISIS route updates
  routing-protocol packets between switches and Quagga
  interface updates from the switches to Quagga.

## Slide 15: RAP
Create tuntap interfaces corresponding to each physical switch port Quagga manages.
translates each RIB entry into two OpenFlow tables
  A Flow table which maps prefixes to entries into a ECMP Group table.
  Multiple flows can share entries in the ECMP Group Table.
Proxy routing-protocol packets between the Quagga control plane
Upon detecting a port state change, RAPd changes the netdev state for each interface change, which propagates to Quagga for routing protocol updates.

## Slide 16: Outline
Background
Design
Traffic Engineering
TE Protocol and OpenFlow
Evaluation

## Slide 17: General Architecture
TE server operates on:
  Network Topology: a graph represents sites as vertices and site to site connectivity as edges.
  Flow Group (FG): a {source site, dest site, QoS} tuple
  A Tunnel (T) represents a site-level path
  A Tunnel Group (TG) maps FGs to a set of tunnels and corresponding weights.
Output Tunnel Groups to SDN gateway, gateway forwards Tunnels and Flow Groups to OFC and install on Switch using Open Flow

## Slide 18: Bandwidth Function
Application’s bandwidth function
  bandwidth allocation to an application given the flow’s relative priority (called fair share)
FG’s bandwidth function
  Piecewise linear additive composition of per-application bandwidth functions.

## Slide 19: Example
Bandwidth enforcer measures
  App1 demand: 15Gbps A  B
  App2 demand: 5Gbps AB
  App3 demand: 10Gbps AC
FG1=App1+App2
FG2=App3

## Slide 20: Tunnel Group Generation
A greedy algorithm
  allocates edge capacity among FGs according to their bandwidth function such that all competing FGs on an edge either receive equal fair share or fully satisfy their demand.
  iterates by finding the bottleneck edge when filling all FGs together by increasing their fair share on their preferred tunnel.
    freeze all tunnels cross the bottleneck edge, move to the next preferred tunnel.

## Slide 21: Example
Tx,y: yth most preferred tunnel for FGx.
T1,1=AB, T2,1=AC, at share 0.90. AB becomes bottleneck
T1,2=ACB, at share 3.33, AC becomes bottleneck

## Slide 22: Example
T1,3=ADCB, T2,2=ADC, at share 10,
FG2 is allocated a fair share of 10 while FG1 is allocated infinite fair share as its demand is fully satisfied

## Slide 23: Tunnel Group Quantization
Example
  split the above allocation in multiples of 0.5
  FG2, (0.3, 0.7)  (0.0, 1.0)
  FG1, (0.5, 0.4, 0.1)  (0.5, 0.5, 0.0)

## Slide 24: Outline
Background
Design
Traffic Engineering
TE Protocol and OpenFlow
Evaluation

## Slide 25: TE State and OpenFlow
A switch maps packets to an FG when their destination IP address matches the prefixes associated with the FG.
Each incoming packet hashes to one of the Tunnels associated with the TG in the desired ratio.
Source site switches encapsulate the packet with an outer IP header whose destination IP address uniquely identifies the tunnel.
  The outer destination-IP address is a tunnel-ID rather than an actual destination.

## Slide 26: Example

## Slide 27: Example
Half the flows are encapsulated with outer IP src/dest IP addresses 2.0.0.1, 4.0.0.1 and forwarded along the shortest path
The remaining flows are encapsulated with the label 2.0.0.1, 3.0.0.1 and forwarded through a transit site.
After decapsulation, the switch forwards to the destination based on the inner packet header, using Longest Prefix Match (LPM) entries (from BGP)

## Slide 28: Composing Routing with TE
Routing/BGP populates the LPM table with appropriate entries
TE uses the Access Control List (ACL) table to set its desired forwarding behavior.
Incoming packets match against both tables in parallel. ACL rules take strict precedence over LPM entries.

## Slide 29: Example

## Slide 30: Example
The LPM entry indicates that the packet should be forwarded through output port 2 without tunneling.
ACL entry takes precedence and indexes into a third table, the Multipath Table, at index 0 with 2 entries.
in parallel, the switch hashes the packet header contents, modulo the number of entries output by the ACL entry.
  i.e., ECMP hashing
distributing flows destined to 9.0.0.0/24 evenly between two tunnels.

## Slide 31: Coordinating TE States Across Sites
TE optimization output to a per-site Traffic Engineering Database (TED)
  key-value datastore for global Tunnels, Tunnel Groups, and Flow Groups.
Compute per-site TED based on TGs, FGs, and Tunnels output by the TE algorithm.
  a single TE operation (TE op) can add/delete/modify exactly one TED entry
The OFC converts the TE op to flow-programming instructions at all devices in that site.

## Slide 32: Example
Dependence
  Configure tunnel before TG and FG
  Cannot delete tunnel before removing affected entries

## Slide 33: Outline
Background
Design
Traffic Engineering
TE Protocol and OpenFlow
Evaluation

## Slide 34: Deployment and Evolution
links are susceptible to frequent port flaps and benefit from dynamic centralized management.
B4 traffic growth
B4 topology change

## Slide 35: TE Ops Performance

## Slide 36: TE Ops Performance

## Slide 37: Impact of Failures
observed traffic between two sites and measured the duration of any packet loss after six types of events:
the failure of a transit router that is a neighbor to an encap router requires a much longer convergence time

## Slide 38: TE Algorithm Evaluation
(a) assume a 1/64 path-split quantum, to focus on sensitivity to the number of available paths.
(b) fix the maximum number of paths at 4, to show the impact of path-split quantum

## Slide 39: Link Utilization and Hashing
100% utilization
ratio of high priority to low priority packets, and packet-drop fractions for each priority.

## Slide 40: Review
Why Google wants to build a WAN?
B4 network’s system architecture.
  Each site
  Global layer
TE algorithm
Forwarding rules